## Slide 1: Webinar series
Monday, July 14th, 10:00–12:00 PDT: An introduction to the Herschel Space Observatory and its Archive
Tuesday, July 15th, 10:00–12:00 PDT: An introduction to photometry with SPIRE
Wednesday, July 16th, 10:00–12:00 PDT: An introduction to photometry and spectroscopy with PACS
Thursday, July 24th, 10:00–12:00 PDT: An introduction to spectroscopy with HIFI
Wednesday, August 13th, 10:00–12:00 PDT: An introduction to spectroscopy with SPIRE
See https://nhscsci.ipac.caltech.edu/sc/index.php/Workshops/HomePage
FOR QUESTIONS, PLEASE USE THE CHAT BOX

## Slide 2: An introduction to the Herschel Space Observatory
David R. Ardila
User Support coordinator / NHSC Archive Scientist

## Slide 3: This webinar
The webinar series
What is Herschel?
  Instruments
  Capabilities
The Archive
  How to get data
  How to look at data
  Have I been scooped?

## Slide 4: Webinar series
Monday, July 14th, 10:00–12:00 PDT: An introduction to the Herschel Space Observatory and its Archive
Tuesday, July 15th, 10:00–12:00 PDT: An introduction to photometry with SPIRE
Wednesday, July 16th, 10:00–12:00 PDT: An introduction to photometry and spectroscopy with PACS
Thursday, July 24th, 10:00–12:00 PDT: An introduction to spectroscopy with HIFI
Wednesday, August 13th, 10:00–12:00 PDT: An introduction to spectroscopy with SPIRE
See https://nhscsci.ipac.caltech.edu/sc/index.php/Workshops/HomePage

## Slide 5: The Herschel Space Observatory
3.5-m cryogenically cooled telescope, located in L2 – Range: 55 – 650 mic
Telescope launched in May 2009. Cryogenic exhaustion in April 2013. No warm mission.
European Space Agency
– led mission with
participation by many
countries, including the US

## Slide 6: NHSC / HSC and all that
NASA Herschel Science Center (NHSC): Established in 2001 at the Infrared Processing and Analysis Center (IPAC), part of Caltech.
  Mission: To provide support to the US-based astronomical community for the exploitation of Herschel data. See http://herschel.caltech.edu
Herschel Science Centre (HSC): Main ESA science center for Herschel, located in Spain. See http://www.cosmos.esa.int/web/herschel/home

## Slide 7
https://nhscsci.ipac.caltech.edu/sc/

## Slide 8
http://www.cosmos.esa.int/web/herschel/home

## Slide 9
’
’

## Slide 13: Photometric performance
From http://www.stsci.edu/jwst/science/sensitivity/newbigpic.jpg

## Slide 21: Program Calls (5/2009 – 4/2013)
One Open Time Key Program call (KPOT)
One Guaranteed Time Key Program call (KPGT)
Two regular Open Time calls (OT1, OT2)
Two regular Guaranteed Time calls (GT1, GT2)
One Science demonstration phase program call, to produce early results (SDP)
A “must-do” program call to fill potential science gaps (DDT_mustdo)
A filler program to observe where nothing else is available (OBS)
Other: DDT programs, ToO programs, Calibration programs, validation programs, etc

## Slide 22: Approved Programs
https://nhscsci.ipac.caltech.edu/sc/index.php/ObsStatus/HomePage
Notes: Demo

## Slide 23: Looking at the Archive
~40,000 observations and over 20000 hours. About 10% of the sky
Everything is public now (except for some calibration observations)

## Slide 24: The Archive
Herschel @ IPAC

## Slide 25: Key Programs
42 large programs submitted at the beginning of the mission. 40% of all time in Herschel.
Two kinds:
  Open Time Key Programs (KPOT - The community)
  Guaranteed Time Key Programs (KPGT - Instrument groups)
Required to produce User Provided Data Products (UPDPs) : High level products with custom processing.
Notes: Demo

## Slide 26
http://www.cosmos.esa.int/web/herschel/key-programmes

## Slide 27: There are counterparts to Spitzer Legacy programs
Spitzer’ SINGS (The Spitzer Infrared Nearby Galaxies Survey - Physics of the Star-Forming ISM and Galaxy Evolution)  Herschel Kingfish (Key Insights on Nearby Galaxies: A Far-Infrared Survey with Herschel)
Spitzer’s GLIMPSE and MIPSGAL  Herschel’s Hi-Gal (The Herschel infrared Galactic Plane Survey)
Spitzer’s C2D  Herschel’s DIGIT
Spitzer’s FEPS  Herschel’s GASPS

## Slide 28: Some user provided data products are already available
http://www.cosmos.esa.int/web/herschel/user-provided-data-products

## Slide 29: What’s in the archive…
Each observation done by Herschel
  All are run through a reduction pipeline
  The products of the pipeline may or may not be what you want. If you want to do photometry of isolated point source you are done!
The user-provided data products submitted by KP
  These can be anything: tables, images, 1D spectra
You will not find catalogs (unless part of a UPDP) or extracted photometry or line measurements. But maybe this will change…

## Slide 30: I will tell you about…
The Herschel Publications Tool
The Herschel Archive User Interface
The Herschel Observing Log
HSPOT: The observation planning tool
The Herschel Interactive Analysis Environment (HIPE)

## Slide 31: How to know if you have been scooped?
Links to refereed papers. These are manually vetted!
https://nhscsci.ipac.caltech.edu/sc/index.php/ObsStatus/HomePage
Notes: Demo

## Slide 32: Publications list
Refereed publications after launch
Hand-checked
No name resolution

## Slide 33: Some lingo
OBSID: A unique 10-digit identifier for the observation
Proposal: Each proposal is identified with a unique string:
  Program_FirstInitialLastNameXX_number
  For example: OT2_dardila_2, AOTVAL_cwilso01_2
Programs:
  OT: Open time; GT: Guaranteed time; DDT: Director’s Discretionary Time; TOO: Target of Opportunity; KP: Key Program; AOTVAL: AOT validation; OBS: Filler program; SDP: Science Demonstration Phase

## Slide 34: Using the Herschel Archive User Interface – HUI
Double-Click the Archive link: “Herschel Science Archive (HSA)”
HSC webpage: http://www.cosmos.esa.int/web/herschel/home

## Slide 36: Things that will be possible within 6 months
I want to find all PACS observations of the CII line for list of targets:
  HSA 6.1 will allow for much more sophisticated searches.

## Slide 37: More Lingo…
AOT: Astronomical Observation Template
  The name of the observing mode used
AOR: Astronomical Observation Request
OD: Operational Day
  The day the observation was done, from 120 to 1446
SPG: Standard Product Generation
  The pipeline version, updated every year. Currently 11.1
QC State: Manual quality control verification – Failed, Pending, Passed, <blank>

## Slide 38: More lingo…Levels
Level 0: Raw data, minimally manipulated.
Also level 0.5
Level 1: Detector readouts converted to physical units.
Also level 1.5
Level 2: Science-quality products. All good observations should have data to level 2. If the level 2 is not present something went very wrong.
Level 2.5:
  SPIRE Phot: Pairs of scan maps taken in the nominal and orthogonal directions
  PACS Phot: Maps combining scan and cross-scan AORs taken on the same sky field
  (v . 13.1) PACS spec: Combination of two observations obtained on-target and on a nearby reference off-position in the unchopped range scan observing mode
  HIFI maps: Regridded cubes for each of the polarizations and backend sub-bands associated to a given observation
  HIFI spectral scans: Deconvolved level-2 spectra
Level 3 (PACS and SPIRE): They are image mosaics obtained by merging all or a subset of contiguous observations belonging to the same proposal with at least a minimum degree of overlap

## Slide 39: Data are downloaded in standard FITS files
These directories are:
BIG: 500 MB for a small PACS observation, if you download all the products
Take a long time to download
With these method, you should download only individual levels
The whole thing is called an Observation Context
The folders within are called products

## Slide 40: The FITS are multi-extension files
Example: This typical PACS photo level-2 file has 8 extensions (four images and four tables)
FV output

## Slide 41: What are all those files?
Data Reduction Help system:
  http://herschel.esac.esa.int/hcss-doc-12.0/
Product Definition Document:
  http://herschel.esac.esa.int/hcss-doc-12.0/index.jsp#pdd:_start

## Slide 42: Astro. Obs. Templates: PACS
PACS Phot
  Point source photometry: deprecated early in the mission
  Scan map photometry
    For point-sources
    For small and large fields
    For the PACS/SPIRE parallel mode
PACS Spec: Integral field spectrograph
  Line spectroscopy: Spectroscopy over narrow pre-defined wavelength ranges, 0.35 to 1.8 mic
  Range spectroscopy: Spectroscopy over arbitrary ranges
AOTs Parallel Mode
PACS and SPIRE photometry of almost the same field at almost the same time.

## Slide 43: AOTs SPIRE
SPIRE Phot:
  Large map
  Small map
  Point source: deprecated early in the mission
SPIRE Spec:
  Single AOT controls spatial coverage, sampling and spectral resolution. Spectral maps are possible.
AOTs HIFI
Single point
Mapping
Spectral scan: Wide spectral regions

## Slide 44: The Herschel Observing Log
Double-click on Observing Log
HSC webpage: http://www.cosmos.esa.int/web/herschel/home

## Slide 45: Observing Log: good but limited…
Searches by science category!
No name resolution
http://herschel.esac.esa.int/logrepgen/observationlist.do
Notes: Good but limited

## Slide 46: HSPOT: The observation planning tool
Originally used to prepare observations to be sent to Herschel
Good learning tool to understand Herschel observations. Very valuable to understand HIFI in particular
You can learn what the AOR parameters mean
Get it from ftp://ftp.sciops.esa.int/pub/hspot/HSpot_download.html
Liaison Activities

## Slide 47: HSPOT

## Slide 48: The Herschel Interactive Processing Environment (HIPE)
HIPE is the software used to re-process data, but it also has strong display and analysis capabilities geared to Herschel.
It allows scripts and GUI work.
HIPE does many, many things in many different ways, and it can be a little bit overwhelming.
Available from http://www.cosmos.esa.int/web/herschel/hipe-download

## Slide 51: The story so far…
Data can be downloaded from HUI using
  “Retrieve Data” -> Tarball. Big. Use to retrieve fragments of observation context only.
  “Send to External Application” -> send to HIPE (reference pointers only aka ‘lazy loading’). Good for inspection and reduction.
  Directly from HIPE: Var=getObservation(obsid,useHsa=True)
Data can also be downloaded from IRSA
To understand what the observer was thinking, load the program in HSPOT
A list of all observations is available from the Observing Log.
A list of publications can be obtained from the Publications Tool
Notes: Add save with fits, no spire, registration, on demand

## Slide 52: The Herschel portal at IRSA
Notes: Demo

## Slide 53: What NHSC can do for you:
We organize webinars such as this. We also organize in-person workshops
We will provide technical support on instruments, data reduction, documentation, via the helpdesk: http://nhsc.ipac.caltech.edu/helpdesk/index.php
We can host members of your team in Pasadena, for intensive data reduction sessions
We produce a monthly newsletter: http://www.herschel.caltech.edu/newsletters

## Slide 56
NHSC Resources | New User? | Expert User? | Comments
NHSC Helpdesk | Y | Y | nhsc.ipac.caltech.edu/helpdesk
NHSC Wiki pages | Y | Y | nhscsci.ipac.caltech.edu
NHSc Newsletter | Y | Y | www.herschel.caltech.edu/newsletters
Webinars | Y | Y | On-line topical discussion groups
Online videos and tutorial | Y | Y | Step by step guides
Introductory Workshops | Y | N | Best for new users
NHSC in-person visits | N | Y | Subject to staff availability
Remote access computers | N | Y | Requested via the helpdesk

## Slide 57: Webinar series
Monday, July 14th, 10:00–12:00 PDT: An introduction to the Herschel Space Observatory and its Archive
Tuesday, July 15th, 10:00–12:00 PDT: An introduction to photometry with SPIRE
Wednesday, July 16th, 10:00–12:00 PDT: An introduction to photometry and spectroscopy with PACS
Thursday, July 24th, 10:00–12:00 PDT: An introduction to spectroscopy with HIFI
Wednesday, August 13th, 10:00–12:00 PDT: An introduction to spectroscopy with SPIRE
See https://nhscsci.ipac.caltech.edu/sc/index.php/Workshops/HomePage

## Slide 58: Web Resources

## Slide 59: Learn more!
Lots of videos in youtube

## Slide 60: Instrument Manuals
All about Herschel: http://herschel.esac.esa.int/twiki/bin/view/Public/SpacecraftObservatoryWeb?template=viewprint
All about PACS: http://herschel.esac.esa.int/twiki/bin/view/Public/PacsCalibrationWeb?template=viewprint
All about SPIRE: http://herschel.esac.esa.int/twiki/bin/view/Public/SpireCalibrationWeb?template=viewprint
All about Parallel mode: http://herschel.esac.esa.int/Docs/PMODE/html/parallel_om.html
All about HIFI: http://herschel.esac.esa.int/twiki/bin/view/Public/HifiCalibrationWeb?template=viewprint

## Slide 61: Data Manuals
All about HIPE, PACS, SPIRE, HIFI data reduction guides: http://www.cosmos.esa.int/web/herschel/data-processing-overview
Scripting help: http://herschel.esac.esa.int/hcss-doc-12.0/